## Slide 1: Pcb information's
Caliber virtual technologies

## Slide 3
Components identification
Function of components
Connection of components
Type of components
Ratings based on application
Electrical specifications of product.

## Slide 4
Circuit design
Components selection
Datasheet identification
Function testing
Package selection / foot print selection
Component placement

## Slide 5
Layer selection
Routing / pad / width selection
Mechanical dimensions
Gerber file generation / viewer
Components assembling /soldring
Testing.

## Slide 6
Trouble shooting
Continuity test , short , open , damage track , dry solder
Section identification / isolation .
Components function / value testing
Connector / coupler testing .

## Slide 7
What are the main steps involved in designing a PCB, from schematic creation to manufacturing?
What is the difference between single-layer, double-layer, and multilayer PCBs?
What are footprints, and how do you verify that a footprint matches a component?
What factors should you consider when placing components on a PCB?
How do you select trace width for a given current?
What are vias? Explain through-hole, blind, and buried vias.

## Slide 8
Why is a ground plane important in PCB design?
What are decoupling capacitors, and where should they be placed?
How would you arrange analog and digital circuits on the same PCB to reduce noise?
What are ERC and DRC, and what types of errors do they detect?
What are Gerber files, drill files, and a BOM? Why are they required?
What is the difference between SMD and through-hole components?

## Slide 9
What causes electromagnetic interference (EMI), and how can PCB layout reduce it?
What is a differential pair, and what routing precautions does it require?
What is controlled impedance, and when is it necessary?
What layout precautions would you take when designing a switching power supply PCB?
How can you manage heat from power components on a PCB?

## Slide 10
A newly assembled PCB draws excessive current. How would you troubleshoot it?
A microcontroller works on a development board but repeatedly resets on your custom PCB. What would you check?
Before sending a PCB for fabrication and assembly, what checks would you perform?

## Slide 11
1. What are the main steps involved in designing a PCB?
Define requirements → select components → create the schematic → check ERC → assign footprints → set board dimensions and design rules → place components → route traces → run DRC → generate manufacturing files → assemble and test.
2. What is the difference between single-layer, double-layer, and multilayer PCBs?
Single-layer: One copper layer; suitable for simple circuits.
Double-layer: Two copper layers connected using vias; suitable for moderately complex circuits.
Multilayer: Several copper layers, often including dedicated power and ground planes; suitable for dense or high-speed circuits.

## Slide 12
What are footprints, and how do you verify them?
A footprint defines a component’s pads, outline, and placement information on the PCB. Verify its dimensions, pad spacing, pin numbering, orientation, and recommended land pattern against the component datasheet.
4. What factors matter during component placement?
Consider signal flow, connector access, short connections, decoupling capacitor locations, heat dissipation, mechanical clearance, and assembly requirements. Keep noisy switching circuits away from sensitive analog circuits.

## Slide 13
5. How do you select trace width for a given current?
Trace width depends on current, copper thickness, allowable temperature rise, and whether the trace is on an internal or external layer. Use an appropriate trace-width calculator, then check voltage drop and manufacturer limits.
6. What are vias?
Vias electrically connect copper layers.
Through-hole via: Passes through the entire board.
Blind via: Connects an outer layer to an internal layer.
Buried via: Connects internal layers without reaching either outer surface.

## Slide 14
7. Why is a ground plane important?
A ground plane provides a low-impedance reference and a return path for signals. A continuous plane helps reduce noise, signal loop area, and EMI.
8. What are decoupling capacitors, and where should they be placed?
They supply brief bursts of current locally and help suppress supply noise. Place them close to IC power pins with short power and ground connections. Follow the datasheet for capacitor values and placement.

## Slide 15
9. How do you reduce noise between analog and digital circuits?
Group components by function, keep switching circuits away from sensitive analog inputs, and control return-current paths. A continuous ground plane is usually preferable; avoid routing signals across ground-plane gaps.
10. What are ERC and DRC?
ERC—Electrical Rule Check: Detects schematic issues such as conflicting pin types or missing connections.
DRC—Design Rule Check: Detects PCB issues such as insufficient clearance, narrow traces, or unconnected nets.
Neither check guarantees that the circuit will function correctly.

## Slide 16
11. What are Gerber files, drill files, and a BOM?
Gerber files: Describe manufacturing layers, including copper, solder mask, and silkscreen.
Drill files: Specify hole sizes and locations.
BOM—Bill of Materials: Lists components, quantities, reference designators, and part numbers.
12. What is the difference between SMD and through-hole components?
SMD components mount on surface pads and support compact layouts and automated assembly. Through-hole components have leads inserted through holes and are often used where stronger mechanical attachment is needed.

## Slide 17
13. What causes EMI, and how can PCB layout reduce it?
Fast switching edges, large current loops, and poor return paths can generate EMI. Reduce it using compact switching loops, continuous reference planes, proper decoupling, and careful routing.
14. What is a differential pair?
A differential pair carries information as the voltage difference between two signals. Route the traces with controlled geometry, a consistent reference plane, and length matching where the interface requires it.

## Slide 18
15. What is controlled impedance?
Controlled impedance means designing a trace’s geometry and board stack-up to achieve a specified characteristic impedance. It is important for high-speed or RF signals, such as USB, Ethernet, and antenna connections.
16. What precautions are needed for switching power supply layouts?
Minimize high-current switching loops, place input capacitors close to switching devices, and keep the switch node compact. Route feedback away from noisy nodes and follow the regulator’s recommended layout.

## Slide 19
How do you manage heat on a PCB?
Use adequate copper area, thermal vias, suitable component spacing, and heatsinks where needed. Estimate component power dissipation and verify temperatures under the expected load and ambient conditions.
18. A new PCB draws excessive current. How would you troubleshoot it?
Disconnect power and inspect for solder bridges, reversed components, and incorrect parts. Check resistance between supply and ground, then power the board using a current-limited supply and isolate circuit sections to locate the fault.

## Slide 20
19. A microcontroller repeatedly resets on a custom PCB. What would you check?
Check supply voltage at the MCU during operation, decoupling, regulator capacity, reset-pin circuitry, clock connections, and boot-pin states. Also inspect firmware reset causes, watchdog settings, solder joints, and noise from connected loads.
20. What checks should you perform before fabrication and assembly?
Verify schematic connections, footprints, pin numbering, polarity, board dimensions, mounting holes, clearances, and trace widths. Run ERC and DRC, inspect manufacturing files in a viewer, and confirm the BOM and component placement files match the final design.